All-NEW Ford FOCUS ST Specifications

Performance and Economy

| Focus ST 5-door |  |  | Fuel consumption l/100 km (mpg) | Performance |
| --- | --- | --- | --- | --- |
| Petrol engines | Power PS | CO2 g/km | Urban | Extra Urban | Combined | Max speed km/h | 0-100 km/h sec | 50-100 km/h sec* |
| 2.3 EcoBoost 6-speed manual | 280 | 179 | 10.8 | 6.2 | 7.9 | 250 | 5.7 | 4.0 |
| 2.0 EcoBlue 6-speed manual | 190 | 125 | 5.9 | 4.2 | 4.8 | 220 | 7.6 | 7.3 |

| Focus ST wagon |  |  | Fuel consumption l/100 km (mpg) | Performance |
| --- | --- | --- | --- | --- |
| Petrol engines | Power PS | CO2 g/km | Urban | Extra Urban | Combined | Max speed km/h | 0-100 km/h sec | 50-100 km/h sec* |
| 2.3 EcoBoost 6-speed manual | 280 | 179 | 10.8 | 6.2 | 7.9 | 250 | 5.8 | TBC |
| 2.0 EcoBlue 6-speed manual | 190 | 125 | 5.9 | 4.2 | 4.8 | 220 | 7.7 | TBC |

* In 4th gear

WEIGHTS AND DIMENSIONS

Weights

| Focus ST 5-door |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) |
| 2.3 EcoBoost 280 PS 6-speed manual | 1508 | 2000 | 3600 | 1600 | 750 |
| 2.0 EcoBlue 190 PS 6-speed manual | 1548 | 2040 | 3840 | 1800 | 750 |

| Focus ST wagon |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Kerb weight (kg)** | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) |
| 2.3 EcoBoost 280 PS 6-speed manual | 1543 | 2065 | 3665 | 1600 | 750 |
| 2.0 EcoBlue 190 PS 6-speed manual | 1585 | 2105 | 3905 | 1800 | 750 |

** Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90 per cent fuel levels, subject to manufacturing tolerances and options, etc., fitted. Weights represent base model specification.

Towing limits quoted represent the maximum towing ability of the vehicle at its Gross Vehicle Mass to restart on a 12 per cent gradient at sea level. The performance and economy of all models will be reduced when used for towing.  Gross Train Mass includes trailer weight.

Dimensions

| Dimensions (mm) | Focus ST 5-door | Focus ST wagon |
| --- | --- | --- |
| Exterior |  |  |
| Overall length | 4388 | 4668 |
| Overall width with/without/folded mirrors | 1979/1825/1848 | 1979/1825/1848 |
| Overall height (including antenna) | 1458 | 1492 |
| Wheelbase | 2700 | 2700 |
| Front track | 1567 | 1567 |
| Rear track | 1556 | 1556 |
| Front overhang | 908 | 909 |
| Rear overhang | 780 | 1059 |
| Min ground clearance (unloaded) | 120 | 118 |
| Min ground clearance (loaded) | 103 | 101 |
| Interior |  |  |
| Front headroom | 987 | 987 |
| Front max legroom | 1109 | 1109 |
| Front shoulder room | 1421 | 1421 |
| Front hip room | 1364 | 1364 |
| Rear headroom | 965 | 1008 |
| Rear legroom | 918 | 918 |
| Rear shoulder room | 1395 | 1395 |
| Rear hip room | 1325 | 1325 |
| Luggage capacity (litres) ‡ |  |  |
| 5-seat mode, laden to package tray (with full size spare) | N/A | 541 |
| 5-seat mode, laden to package tray (with mini spare) | 273 | 575 |
| 5-seat mode, laden to package tray (with tyre repair kit) | 375 | 608 |
| 2-seat mode, laden to roof (with full size spare) | N/A | 1576 |
| 2-seat mode, laden to roof (with mini spare) | 1250 | 1620 |
| 2-seat mode, laden to roof (with tyre repair kit) | 1354 | 1653 |
| Luggage compartment dimensions (mm) |  |  |
| Load length at floor to 1st row | 1568 | 1835 |
| Load length at floor to 2nd row | 788 | 1047 |
| Load width between wheelhouses | 1016 | 1150 |
| Load opening width (max) | 1018 | 1051 |
| Load opening width (floor) | 998 | 1078 |
| Load opening height | 613 | 702 |
| Lift-over height (kerb) | 667 | 626 |
| Fuel tank capacity (litres) |  |  |
| Petrol/Diesel | 52/47 | 52/47 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted. Dimensions represent base model specification.

PERFORMANCE TECHNOLOGIES#

Drive Modes – Slippery/Wet, Normal, Sport, Track

Launch Control

Rev-matching

Shift indicator light

DRIVER ASSISTANCE TECHNOLOGIES#

Active Park Assist 2 with Park-Out Assist

Adaptive Cruise Control with Stop & Go, Speed Sign Recognition and Lane-Centring

Adaptive Front Lighting System with Predictive curve light and Sign-based light

Adjustable Speed Limiter

Auto High Beam

Blind Spot Information System

Cross Traffic Alert with Active Braking

Distance Indication

Driver Alert

Evasive Steering Assist

Forward Collision Warning

Front and Rear Park Aid

Glare-free high beam

Head-up display

Hill Launch Assist

Intelligent Speed Limiter

Lane Keeping Aid

Lane Keeping Alert

Post-Collision Braking

Pre-Collision Assist with Pedestrian and Cyclist Detection

Rear wide-view camera

Traffic Sign Recognition

Wrong Way Alert

COMFORT AND CONVENIENCE#

B&O PLAY Sound System

Easy Fold Seats

Electric parking brake

FordPass Connect embedded modem

Hands-free tailgate

Heated steering wheel

Openable panorama roof

Rotary gear shift dial

SYNC 3 with 8-inch touchscreen

Wireless charging pad

#Dependent on vehicle specification and options selected. Some features available only in combination with 7-speed automatic transmission to be offered later in 2019

STEERING

| System | Rack and pinion with column-mounted electronic-power assisted steering module. Steering Torque Disturbance Reduction software |
| --- | --- |
| Ratio | 11.6:1 |
| Turning circle (m) kerb-to-kerb | 11.3 |

CHASSIS

| Front suspension | Independent MacPherson struts with offset coil spring over gas filled twin-tube damper units (triple-tube for CCD) and lower L-arms with optimised front and rear rubber bushings mounted on separate reinforced cross-member sub-frame. Unique Focus ST anti-roll bar, steering knuckle geometry, spring and damper tuning. Continuously Controlled Damping for 5-door models (standard for 2.3-litre EcoBoost, optional for 2.0-litre EcoBlue) |
| --- | --- |
| Rear suspension | Short-long-arm, multi-link independent geometry with isolated subframe. Unique geometry for wagon models. Twin-tube rear damper (triple-tube for CCD) with optimised dual path body mounts. Unique Focus ST spring and damper tuning. Continuously Controlled Damping for 5-door models (standard for 2.3-litre EcoBoost, optional for 2.0-litre EcoBlue) |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Hydraulically operated dual-circuit system with diagonal distribution and Electric Brake Booster. Vented front discs. Solid rear discs. Electronic four-channel anti-lock braking system (ABS) with electronic brake-force distribution (EBD), Electronic Stability Program (ESP) and Emergency Brake Assist (EBA). Autonomous emergency braking (AEB) as part of Pre-Collision Assist with Pedestrian and Cyclist Detection. |
| Disc dimensions (mm) | Ø330 x 27 | Ø302 x 11 |
| Piston dimensions (mm) | 2 x Ø44 | Ø36 or Ø38 |

WHEELS & TYRES

8 x 18-inch with 235/40 R18 Michelin Pilot Sport 4S tyres

8 x 19-inch with 235/35 R19 Michelin Pilot Sport 4S tyres

PETROL ENGINES

|  |  | 2.3-litre EcoBoost (280 PS) |
| --- | --- | --- |
| Type |  | Inline four cylinder petrol, turbocharged, transverse |
| Displacement | cm3 | 2,261 |
| Bore | Mm | 87.6 |
| Stroke | Mm | 94.0 |
| Compression ratio |  | 10.0:1 |
| Max power | PS (kW) | 280 (206) |
|  | at rpm | 5500 |
| Max torque | Nm | 420 |
|  | at rpm | 3000-4000 |
| Valve gear |  | DOHC with 4 valves per cylinder |
| Cylinders |  | 4 in-line |
| Cylinder head |  | Cast aluminium |
| Cylinder block |  | Cast aluminium |
| Camshaft drive |  | Twin independent variable cam timing |
| Crankshaft |  | Forged steel, 8 counterweights, 5 main bearings |
| Engine management |  | Bosch MED17 with CAN-Bus and individual cylinder knock control. FGEC software |
| Fuel injection |  | High pressure direct fuel injection |
| Emission level |  | Euro 6d-TEMP |
| Emission control |  | Gasoline particulate filter |
| Turbocharger |  | Low-inertia twin-scroll fixed geometry turbo charger; electronically actuated waste-gate; anti-lag |
| Lubrication system |  | Pressure-fed with mechanical oil pump |
| Cooling system |  | Water pump with thermostat and valves, with thermal management system |
| Transmission |  | 6-speed manual |
| Gear ratios |  | 6th 0.686 5th 0.821 4th 1.029 3rd 1.321 2nd 1.952 1st 3.231 Reverse 3.343 FDR: 4.063 |

DIESEL ENGINES

|  |  | 2.0-litre EcoBlue (190 PS) |
| --- | --- | --- |
| Type |  | Inline four cylinder turbo diesel, transverse |
| Displacement | cm3 | 1996 |
| Bore | Mm | 84.0 |
| Stroke | Mm | 90.0 |
| Compression ratio |  | 16.0:1 |
| Max power | PS (kW) | 190 (140) |
|  | at rpm | 3500 |
| Max torque | Nm | 400 |
|  | at rpm | 2000 |
| Valve gear |  | DOHC with 4 valves per cylinder |
| Cylinders |  | 4 inline |
| Cylinder head |  | Cast aluminium |
| Cylinder block |  | Cast iron |
| Camshaft drive |  | Twin -pulley low-friction belt-in-oil with dynamic tensioner |
| Crankshaft |  | Forged steel, 4 counter-weights, 5 main bearings |
| Engine management |  | Ford Common Rail Diesel Engine Management System |
| Fuel injection |  | Common rail direct fuel injection; 8-hole piezo-electric injectors |
| Emission level |  | Euro 6d-TEMP |
| Emission control |  | High- and low-pressure exhaust gas recirculation; water-air charge cooling; selective catalytic reduction after treatment |
| Turbocharger |  | Low-inertia variable geometry turbocharger with electronic control |
| Lubrication system |  | Pressure-fed lubrication system with full flow oil filter, variable displacement oil pump |
| Cooling system |  | Engine driven water pump with thermostat control |
| Transmission |  | 6-speed manual |
| Gear ratios |  | 6th 0.536 5th 0.644 4th 0.816 3rd 1.156 2nd 1.864 1st 3.583 Reverse 3.706 FDR 3.813 |

# # #

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

Note: The declared fuel/energy consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel-efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

Since 1 September 2017, certain new vehicles are being type-approved using the World Harmonised Light Vehicle Test Procedure (WLTP) according to (EU) 2017/1151 as last amended, which is a new, more realistic test procedure for measuring fuel consumption and CO2 emissions. Since 1 September 2018 the WLTP has begun replacing the New European Drive Cycle (NEDC), which is the outgoing test procedure. During NEDC Phase-out, WLTP fuel consumption and CO2 emissions are being correlated back to NEDC. There will be some variance to the previous fuel economy and emissions as some elements of the tests have altered i.e., the same car might have different fuel consumption and CO2 emissions.

About Ford Motor Company

Ford Motor Company is a global company based in Dearborn, Michigan. The company designs, manufactures, markets and services a full line of Ford cars, trucks, SUVs, electrified vehicles and Lincoln luxury vehicles, provides financial services through Ford Motor Credit Company and is pursuing leadership positions in electrification, autonomous vehicles and mobility solutions. Ford employs approximately 196,000 people worldwide. For more information regarding Ford, its products and Ford Motor Credit Company, please visit www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 49,000 employees at its wholly owned facilities and approximately 63,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 23 manufacturing facilities (16 wholly owned or consolidated joint venture facilities and seven unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.

| Contact: Kim Benns Ford of Europe +44 (0) 126 840 4837 kbenns@ford.com |  |
| --- | --- |